## Slide 1: Lab Equipment

## Slide 2: Beaker
Beakers hold solids or liquids that will not release gases when reacted or are unlikely to splatter if stirred or heated.

## Slide 3: Erlenmeyer Flask
Erlenmeyer flasks hold solids or liquids that may release gases during a reaction or that are likely to splatter if stirred or heated.

## Slide 4: Florence Flask
Rarely used in first year chemistry, it is used for the mixing of chemicals. Narrow neck prevents splash exposure.

## Slide 5: Graduated Cylinder
A graduated cylinder is used to measure volumes of liquids.

## Slide 6: Gas Collecting Bottle
We use gas collecting bottles when large volumes of gases are produced, and must be collected by the displacement of water.

## Slide 7: Test Tubes
13 x 100 mm test tubes
10 x 75 mm test tubes
Ignition
tube

## Slide 8: Test Tube Holder
A test tube holder is useful for holding a test tube which is too hot to handle.

## Slide 9: Test Tube Brushes
Test tube brushes are used to clean test tubes and graduated cylinders.
Forcing a large brush into a small test tube will often break the tube.

## Slide 10: Test Tube Racks
Test tube racks are for holding and organizing test tubes on the laboratory counter. Plastic racks may melt in contact with very hot test tubes.

## Slide 11: Rubber Stoppers
Rubber stoppers are used to close containers to avoid spillage or contamination.
Containers should never be heated when there is a stopper in place.

## Slide 12: Spot Plates
Spot plates are used when we want to perform many small scale reactions at one time. We will use these many times during the year.

## Slide 13: Watch Glass
A watch glass is used to hold a small amount of solid, such as the product of a reaction.

## Slide 14: Glass Stir Rod
A glass rod is used to manually stir solutions. It can also be used to transfer a single drop of a solution.

## Slide 15: Medicine Dropper
A medicine dropper is used to transfer a small volume of liquid (less than one mL).
On top of each medicine dropper is a “rubber bulb”

## Slide 16: Litmus Paper
Red litmus paper is used to identify bases.
Blue litmus paper is used to identify acids.

## Slide 17: Forceps
Forceps (or tweezers) are used to pick up small objects.

## Slide 18: Funnel
A funnel is used to aid in the transfer of liquid from one vessel to another.

## Slide 19: Mohr Pipet
A Mohr pipet measures and delivers exact volumes of liquids.

## Slide 20: Wash Bottle
A wash bottle has a spout that delivers a wash solution to a specific area. Distilled water is the only liquid that should be used in a wash bottle.

## Slide 21: Weighing Boat
Weighing boats are used to weigh solids that will be transferred to another vessel.

## Slide 22: Spatulas
Spatulas are used to dispense solid chemicals from their containers.
Chemicals should never be transferred with your bare hands.

## Slide 23: Beaker Tongs
Beaker tongs are used to move beakers containing hot liquids

## Slide 24: Bunsen Burner
Bunsen burners are used for the heating of nonvolatile liquids and solids.

## Slide 25: Evaporating Dish
The evaporating dish is used for the heating of stable solid compounds and elements.

## Slide 26: Crucible
Crucibles are used for heating certain solids, particularly metals, to very high temperatures.

## Slide 27: Clay Triangle
The clay triangle is used as a support for porcelain crucibles when being heated over a Bunsen burner.

## Slide 28: Crucible Tongs
For handling hot crucibles; also used to pick up other hot objects. NOT to be used for picking up beakers!

## Slide 29: Glass Plates
Glass plates provide a surface for semi-micro scale experiments, such as drop reactions and testing of acids and bases.

## Slide 30: Triangular File
Triangular files are used primarily to cut glass rod, a skill that your instructor will share with you when it becomes useful.

## Slide 31: Ringstands and their Components
Ringstands are a safe and convenient way to perform reactions that require heating using a Bunsen burner.

## Slide 32: Ringstands and their Components Iron Rings
Iron rings connect to a ringstand and provide a stable, elevated platform for the reaction.

## Slide 33: Ringstands and their Components Utility Clamps
Utility clamps are used to secure test tubes, distillation columns, and burets to the ringstand.

## Slide 34: Ringstands and their Components Double Buret Clamps
Double Buret clamps are used to burets – long graduated tubes used in titration.

## Slide 35: Ringstands and their Components Wire Gauze
Wire gauze sits on the iron ring to provide a place to stand a beaker.
On older wire gauze, the white material is asbestos!

## Slide 36: Pressed Fiber Pad
A 4” x 4” square of ceramic fiber, it provides a surface for hot beakers so that the beaker does not come in contact with a cold countertop and shatter.

## Slide 37: Strikers
Strikers are used to light Bunsen burners.
The flints on strikers are expensive. Do not operate the striker repeatedly just to see the sparks!